## Slide 1: Introduction to IP (Internet Protocol)
Bob Konigsberg
Network Evaluation
Copyright (c) 1998 Network Evaluation
This document may be distributed as long as the copyright notice is left intact.

## Slide 2: Internet Protocol (IP)
Terms and Definitions
IP itself (Addressing, Networks, Subnets)
IP Specifics as used on Win95/NT
IP Based Protocols (TCP, UDP, ICMP)
IP Routing (Static, RIP, IGRP, OSPF)
Brief Introduction to OSI Model
Application Level Protocols

## Slide 3: Terms and Definitions (1)
Network - A set of connected systems that communicate as peers
Host - A specific computer on a network (workstation, server, printer)
internet - A network made of of multiple networks
Internet - The world-wide connection of many smaller internets
Router - A device for connecting administratively separate networks

## Slide 4: Terms and Definitions (2)
Adapter - A circuit card to connect a host (PC) to a network
Media - The type of physical network system (Ethernet, FDDI)
Protocol - A predefined set of behaviors used by network systems
DNS - Domain Name Service; used to identify hosts by name rather than a numeric address.

## Slide 5: IP Address Structure (1)
IP V4 addresses are 32 bits with an address space of 4.2 billion systems (much wasted)
Addresses are divided into Class A, B, C, D
32 bit length is divided into 4, 8 bit values
Shown as 1.2.3.4 or 192.168.99.1
Network portion is assigned to organization
Organization then divides that into subnets

## Slide 6: IP Address Structure (2)
Class A is an 8 bit network number (1-126) with a 24 bit host/subnet address space (125 nets, each with 16+ million addresses)
Class B is a 16 bit network number (128.0 - 191.255) with a 16 bit host/subnet address space (16 thousand networks, each with 65 thousand addresses)
Class C is a 24 bit network number (192.0.0 - 224.255.255) with an 8 bit host/subnet address (2 million networks, with 254 addresses each)
Class D is a special case (ignored for now)

## Slide 7: IP Address Structure (3)
32 bit space shown below
--------.--------.--------.--------
Bldg. 4 router address in decimal and binary notation
192 . 168 . 84 . 1
11000000.10101000.01010100.00000001
24 bit (Class C) subnet mask shown below in decimal and binary notation
11111111.11111111.11111111.00000000
255 . 255 . 255 . 0
The 1’s part is the network number.
The 0’s part is the host address.

## Slide 8: IP Address Structure (4)
32 bit space shown below
--------.--------.--------.--------
A DMZ address space shown below:
From 192. 168 . 213 . 65
to 192. 168 . 213 . 94
11000000.10101000.11010101.01000001
11000000.10101000.11010101.01011110
27 bit subnet mask shown below in decimal and binary notation
11111111.11111111.11111111.11100000
255 . 255 . 255 . 224
Note:broadcast address is 205.227.213.95 (11000000.10101000.11010101.01011111)

## Slide 9: IP Addressing (Workstation View) (1)
  IP Address
  Subnet Mask
  Default Gateway(s)
  DHCP (Dynamic Host Configuration Protocol)
  WINS Server (Or use DHCP Server)
  Bindings (MS Client, NetWare Client, other)
  DNS (Host, Domain, Servers, Domain Suffix)

## Slide 10: IP Addressing (Workstation View) (2)
IP Address must be unique on the entire network
IP Address must belong to local network.
Defines both the network to which a given system belongs, AND identity on the net

## Slide 11: IP Addressing (Workstation View) (3)
Subnet Mask defines the dividing line between other local systems (on the local subnet) and remote systems which must reached through a router
Default Gateway - The router to which all non-local traffic must be sent.
Local traffic is sent directly to the destination

## Slide 12: IP Addressing (Gateways)
Default gateway is generally the local router for a given network.
There may be other routers. If one is needed (to deliver a packet), the default router will inform the workstation by a message called an ICMP Redirect.
As a workstation learns of other routes and routers, it builds a local routing table.
PC’s have a default router since most of them do not participate in routing protocols. (Unix systems can)

## Slide 13: IP Addressing (DHCP)
DHCP (Dynamic Host Configuration Protocol)
  Allows workstations to get their IP address dynamically, in response to a broadcast
  Also supplies Subnet Mask, Default Gateway, DNS server, WINS server and other values on an as-needed basis
  Eliminates the need administer these values by hand
  Eliminates the conflict of duplicate IP Addresses
  SoAndSo has 2 DHCP Servers, Bldg. 1 and Bldg. 4 for both redundancy and better response time.
  Each server has separate ranges to avoid conflicts

## Slide 14: IP Addressing (WINS)
WINS - Windows Internet Naming Service (Internet refers to local internets. WINS can be interoperable with DNS (see below).
WINS is a mechanism for resolving NETBIOS names to IP Addresses
WINS can also be used for resolving IP Addresses obtained through DHCP

## Slide 15: IP Addressing (Bindings)
Bindings refers to what top level clients are making use of the/which protocol stack (TCP/IP, IPX, NetBEUI)
Examples are: Clients for Microsoft networks, NetWare, VPN, NFS, Banyan Vines
One of the protocols must be the default (MS Networking will use that first)

## Slide 16: IP Addressing (DNS) (1)
Each host must have a unique name within the domain or subdomain
  Our domain is soandso.com
  Subdomains include eng.soandso.com
Multiple DNS servers are allowed in a specified search order; allows for redundancy

## Slide 17: IP Addressing (DNS) (2)
Forward DNS lookup gets an IP address for a given name - most common usage
Reverse DNS lookup gets a name for a given IP address - used in traceroute(Unix)/tracert(NT) and in troubleshooting.
Domain suffix allows for default lookups so that the domain doesn’t have to be specified: localweb.soandso.com

## Slide 18: Determining Subnet Values
Subnets are counted from the left of a 32 bit field
Each increment of a subnet mask doubles the number of networks and halves the number of hosts
Expressed as decimal number, but seen by systems as a binary mask (1’s on the left, 0’s on the right)
Base 10 (decimal) uses digits 0-9 and has 1’s, 10’s, 100’s, 1000’s places etc.
Base 2 (binary) uses digits 0-1 and has 1’s, 2’s, 4’s, 8’s, 16’s, 32’s, 64’s, 128’s, places etc.
Subnet masks (decimal) are a representation of a sliding scale moving from left to right

## Slide 19: Comparing Subnet Values
This example assumes a Class B (16 bit) sized network number
Decimal Binary Nets Hosts
255.255.0.0 11111111.11111111.00000000.00000000 1 64K-2
255.255.128.0 11111111.11111111.10000000.00000000 2 32K-2
255.255.192.0 11111111.11111111.11000000.00000000 4 16K-2
255.255.224.0 11111111.11111111.11100000.00000000 8 8190
255.255.240.0 11111111.11111111.11110000.00000000 16 4094
255.255.248.0 11111111.11111111.11111000.00000000 32 2046
255.255.252.0 11111111.11111111.11111100.00000000 64 1022
255.255.254.0 11111111.11111111.11111110.00000000 128 510
255.255.255.0 11111111.11111111.11111111.00000000 254 254
255.255.255.128 11111111.11111111.11111111.10000000 512 126
255.255.255.128 11111111.11111111.11111111.11000000 1024 62
This Example assumes a Class C (24 bit) sized network number
255.255.255.0 11111111.11111111.11111111.00000000 1 254
255.255.255.128 11111111.11111111.11111111.10000000 2 126
255.255.255.192 11111111.11111111.11111111.11000000 4 62
255.255.255.224 11111111.11111111.11111111.11100000 8 30
255.255.255.240 11111111.11111111.11111111.11110000 16 14
255.255.255.248 11111111.11111111.11111111.11111000 32 6
255.255.255.252 11111111.11111111.11111111.11111100 64 2
255.255.255.254 11111111.11111111.11111111.11111110 128 0
255.255.255.255 11111111.11111111.11111111.11111111 0 1

## Slide 20: Subnetting - Basic Planning
Subnets are generally sized to allow room for growth
Balance must be maintained between number of hosts on net and number of nets required to serve the organization
Small subnets are used where the number of possible addresses is very small so as not to waste addressing space.

## Slide 21: Subnetting - Practical Examples
A subnet for a WAN (Wide Area Network) link which contains only 2 devices.
123.45.67.1 and 123.45.67.2 would use a subnet mask of 255.255.255.252 (last octet would be 11111100)
Possible addresses are: 00, 01, 10, 11
123.45.67.0 is the network number itself
123.45.67.1 is the first router
123.45.67.2 is the second router
123.45.67.3 is the broadcast address
NOTE: The broadcast address for any network is all 1’s (binary) in the address field.

## Slide 22: Subnetting - Practical Examples
A subnet for a large building, which contains over 500 devices; 510 hosts isn’t enough room for growth.
192.168.0.0 through 192.168.31.255 are available for use
Subnet mask for 1022 hosts (252.0/11111100.00000000)
In this case, 192.168.0.0 is the network number.
Hosts range from 192.168.0.1 through 192.168.3.254
192.168.0.1 is the first address (probably the router)
123.45.67.2 - 10 is reserved for MIS owned devices
192.168.3.255 is the broadcast address
11000000.10101000.00000011.11111111 (address)
11111111.11111111.11111100.00000000 (netmask)
NOTE: The broadcast address for any network is all 1’s (binary) in the address field.

## Slide 23: Subnetting - Practical Examples
A subnet for a WAN with small offices in each location.
192.168.0.0 through 192.168.31.255 are available for use
Mask for 8 nets, 30 hosts each (255.224/11111111.11100000)
Net numbers: 192.168.4.0, 192.168.4.32, .64, .96, .128, .160, 192, 224
Hosts range from 192.168.4.1 through 192.168.4.30 (31 is broadcast)
192.168.4.33-4.62, 192.168. 4.65-4.94, 192.168. 4.97-4.126,
192.168. 4.129-4.158, 4.161-4.190, 4.193-4.222, 4.225-4.254
192.168.4.xxx11111 is the broadcast address (xxx+31)
11000000.10101000.00000100.xxx11111 (address)
11111111.11111111.11111111.11100000 (netmask)
NOTE: This must be done through 1 router unless a routing protocol is used which permits networks with different subnet masks. (Called VLSM: Variable Length Subnet Masking)

## Slide 24: IP Addressing Schemes
Most organizations reserve address space for IS equipment
  Gateways/Routers
  Hubs, Switches
  DNS Server(s)
  WINS Server(s)
  DHCP Server(s)
  Network Based Printers
  Some of this may be duplicated in different locations

## Slide 25: IP Routing (1)
Network addresses need not be adjacent: Follow the path of a packet from client to server:
Sender 192.168.84.123 (some workstation in B4) to MSEXCH01 (Exchange Server in B1)
Goes to 192.168.84.1 B4 Router Ethernet side
Goes from 192.168.14.2 to 192.168.14.1 (T-1, B4-B1)
192.168.14.1 and 192.168.85.1 are two different ports on the cisco 7514 router in Bldg.1 (1 is T-1, 1 is Ethernet)
Goes from 192.168.85.1 to 192.168.85.111 (MSEXCH01)
Returned packets follow the opposite path back

## Slide 26: IP Routing (2)
How does a router know how (or where) to deliver a packet?
  Routing Tables: Internal lists of different network routes that tell a router what the best path is to any given network
  Default route (Not the same as default router) - Default route tells the router that if it doesn’t find a specific route for a particular packet, to deliver it to the router advertising the default route. This is how our Internet access works.

## Slide 27: IP Routing (3)
Where do routing tables come from?
Static - Each route is manually defined.
  No flexibility, very tedious to maintain
  Used where security or tight control are needed
Dynamic Routing Protocols
  RIP - Routing Information Protocol
  OSPF - Open Shortest Path First
  IS-IS - Router to Router protocol (IS=Intermediate System)
  IGRP - Internet Gateway Routing Protocol
  EIGRP - Enhanced Internet Gateway Routing Protocol

## Slide 28: IP Packet Details - What’s it look like?
Destination/Source MAC addresses
Optional framing (802.2, Ethernet II)
Packet Type: IP (could also be IPX, XNS, OSI, etc.)
Time to live (Number of Router Hops)
Protocol type (UDP, TCP, ICMP, etc.)
Checksum: Recalculated since TTL (Time To Live) changes with each router hop
Protocol specific header (UDP, TCP, ICMP, etc.)
Protocol specific data (Application level)

## Slide 29: TCP/IP
Transmission Control Protocol
Connection Oriented: Awareness of other nodes
Reliability: Guaranteed delivery of data or notification if delivery fails
Efficiency of transport by using sliding windows (No. of packets sent w/o Ack)
Like a telephone call or registered letter

## Slide 30: TCP Packet
MAC and IP Header
TCP Header
  Source Port
  Destination Port
  Sequence Number
  Acknowledgement Number
  Data Offset
  Bits: Urgent, Ack, Push, Reset, Synch, Finish
  Window Size
  Checksum
  Options
  Padding

## Slide 31: TCP Session Setup and Teardown
Initial packet with only SYN bit set
If receiver wants to setup a session, responds with the SYN and ACK bit set (OK, let’s talk).
If NO session desired (e.g. service not running), TCP on “server” responds w/RST bit (go away)
Once session is set up all future packets have ACK bit set.

## Slide 32: TCP Session Setup

## Slide 33: UDP Packet
User Datagram Protocol
Connectionless - No State Information
More like a postcard; The only way you know it got there is when you get a follow up message.
Used for quick lookup or notification, examples: Name Lookup, Syslog messages, SNMP traps, queries

## Slide 34: UDP Packet
Mac and IP Headers
Source Port
Destination Port
Length of packet
Checksum
Application specific data

## Slide 35: ICMP
Internet Control Message Protocol
Used for re-routing, unreachable destinations and flow control
Many types of messages, some with more specifically defined message types.

## Slide 36: Selected ICMP Message Types (1)
0 Echo Reply - Answer to a Ping (Echo Request)
3 Destination Unreachable
  0 Net Unreachable - Router tells you that the (sub)net can’t be reached
  1 Host Unreachable - The destination host may not exist
  3 Port Unreachable - There is no service at that port on the computer
  4 Fragmentation Needed and Don't Fragment was Set
  5 Source Route Failed - Likely a firewall rejection
  6 Destination Network Unknown - The network cannot be found
  9 Communication with Destination Network is Administratively Prohibited
  10 Communication with Destination Host is administratively Prohibited
  11 Destination Network Unreachable for Type of Service
  12 Destination Host Unreachable for Type of Service

## Slide 37: Selected ICMP Message Types (2)
4 Source Quench - Primitive flow control
5 Redirect - Not me, go see this other router
8 Echo (Request) - Ping request
9 Router Advertisement - Hi, I’m a router
11 Time Exceeded - TTL Expired (Traceroute)
13 Timestamp
14 Timestamp Reply
15 Information Request
16 Information Reply
17 Address Mask Request
18 Address Mask Reply
19 Reserved (for Security)
30 Traceroute (ICMP version, not UDP version)

## Slide 38: TraceRoute - Clever Hack
Either Ping, or UDP packet w/port 33,000+ is sent with 1 hop in the TTL field.
When Intermediate device replies w/ICMP type 11 Time exceeded, then packet is resent with the TTL field incremented.
This keeps up until either the destination is reached, OR the max TTL (30) is reached.
Along the way, each destination system is identified by sending ICMP Time Exceeded.
Bottom Line: Exact network path described

## Slide 39: OSI 7 Layer Model

## Slide 40: IP Based Application Protocols
Telnet NTP SNTP TimeOfDay
FTP POP3 DNS Whois
HTTP NetBIOS TACACS SQLServer
SMTP TFTP Gopher RPC
SNMP Auth RealAudio PictureTalk
NNTP X-Windows IRC RPC(Unix/NT)
Rlogin Rsh HTTPS Lotus Notes