## Slide 1: Introduction to Network Protocols
Bob Konigsberg
Network Evaluation
Copyright (c) 1999 Network Evaluation
This document may be distributed as long as the copyright notice is left intact.

## Slide 2: What is a protocol?
An agreed upon standard of behavior
  Good Morning, How are you?
  I’m fine thank you. How are you?
  Uh Huh, I understand.
  That’s right!

## Slide 3: Protocols we use daily
Placement of numbers affects their meaning
  Debits vs. Credits
  Capital Purchases vs.. Expenses
  Gross Pay vs. Withholding Taxes
  To the right or left of the decimal point
Other behaviors
  Which side of the road we drive on
  Language, spelling, etc.

## Slide 4: Network Protocols (1)
The OSI 7 layer model
  Application - Used by applications directly
  Presentation - Provides a structured view based on the network architecture
  Session - Awareness of the state of connection
  Transport - Ability to deliver a message
  Network - Administrative/logical separation
  Datalink - Awareness of other nodes
  Physical - mechanism of connectivity

## Slide 5: Network Protocols (2)
Proprietary Protocols
  Defined by individual companies
  May become semi-public standards
  DECNet, (Digital’s Network protocol)
  XNS (Xerox Network Systems)
  IPX (Novell’s Internet Packet Exchange)

## Slide 6: Network Protocols (3)
Proprietary Protocols (Continued)
  IBM’s SNA (Systems Network Architecture
  AppleTalk/Apple Filing Protocol
  NetBIOS (Originally IBM/Microsoft Network)
  Vines (Banyan Networks
  Token Ring (IBM physical wiring)
  LocalTalk (Apple serial physical wiring)

## Slide 7: Network Protocols (4)
Open Standards
  Defined by consortiums or committees
  TCP/IP Protocol Suite
  OSI Protocol Suite
  Ethernet (10Base2, T, 100Base….)
  FDDI
  ATM

## Slide 8: OSI Model Layer 1 - Physical (1)
Physical Layer defines physical characteristics
Electrical specification - Voltages, current
Optical specification - wavelength, intensity
Physical (connectors, conductors, material, topology)
Timing - Data speed, sequencing, multiplexing
Access method -CSMA/CD, Token Passing
Full Duplex, Half Duplex

## Slide 9: OSI Model Layer 1 - Physical (2)
RS-232 Asynchronous Serial Communication
V.35 Synchronous Serial Communication
Local Talk (Apple High Speed Serial)
Ethernet (10Base2, 10BaseT, 100BaseT…)
Token Ring (4/16 MB/s)
FDDI (100 MB/s)
SONET (Photonic Layer)
HSSI (High Speed Serial Interface) > 1.5 Mb/s

## Slide 10: OSI Model Layer 2 - Datalink (1)
Awareness of Network Addresses (MAC, DCE/DTE, DLCI)
Ability to deliver a packet to another node
Deals with only local network
Bridging/Switching operate at this level, separating traffic based on MAC addresses

## Slide 11: OSI Model Layer 2 - Datalink (2)
NDIS (Network Device Interface Spec)
ODI (Open Datalink Interface)
Frame Relay
Lower portions of the ATM spec
PPP (Point to Point Protocol)
X.25

## Slide 12: OSI Model Layer 3 - Network (1)
Awareness of more than 1 network
Operates at the router (and some switches)
Allows administrative separation of networks
Requires routing protocols (How to get there)
ES (End-System) and IS (Intermediate System)

## Slide 13: OSI Model Layer 3 - Network (2)
XNS (Xerox Network Systems)
IPX (Novell’s NetWare)
IP (Internet Protocol)
DecNet
ISO Protocols
Banyan VINES

## Slide 14: OSI Model Layer 3 - Network (3)
Routing Protocols
  Static Routes - Manually set on each router
  RIP (IP, XNS, IPX) - Distance Vector
    No Knowledge of differing speeds or network structure
    Range of 0 (local) to 15 (unreachable)
    Bases its metric on hop count
  RTMP (AppleTalk)
    Limited capability (No customizing)
    Sees multiple paths as routing loops

## Slide 15: OSI Model Layer 3 - Network (4)
Routing Protocols
  OSPF (IP- Link State), NLSP (IPX- Link State)
    Weights each route according to media rate
    Administratively adjustable
    Propagates network structure (subnet masks)
  IGRP/EIGRP (IP, IPX, AppleTalk, cisco proprietary)
    Weights routes according to media rate
    Propagates network structure (subnet masks)
    Administratively adjustable
    EIGRP also handles VLSM

## Slide 16: OSI Model Layer 3 - Network (5)
Routing Protocols
  IS-IS (Router to Router)
  EGP (Exterior Gateway Protocol)
  BGP (Border Gateway Protocol)
    Security-minded
    For exchanging routing information based on contractual agreements between unrelated parties

## Slide 17: OSI Model Layer 4 - Transport (1)
Deals with moving data across more than 1 network
No guaranteed delivery (Best Effort)
Used for quick messages in which speed and simplicity are more important than reliability
If needed, reliability mechanisms are built in at a higher level (NetWare)

## Slide 18: OSI Model Layer 4 - Transport (2)
IPX (Novell’s Internetwork Packet Exchange)
XNS IDP (XNS Internet Datagram Protocol)
AppleTalk (Phase I and Phase II)
UDP (User Datagram Protocol)
DECNet (Digital Equipment Networks)
Banyan Vines Network Architecture
NetBIOS Datagrams (All underlying protocols)

## Slide 19: OSI Model Layer 5 - Session (1)
Awareness of a connection (Connection Oriented)
Aware of the state of any given connection
Guaranteed delivery or notification of failure
Validation of the quality of data received (checksums)

## Slide 20: OSI Model Layer 5 - Session (2)
NetWare's SPX (Sequenced Packet Exchange)
Xerox’s SPP (Sequenced Packet Protocol)
IP’s TCP (Transmission Control Protocol)

## Slide 21: OSI Model Layer 6 - Presentation (1)
Presents a picture of the network independent of underlying protocols
Used to abstract system model for a service-oriented picture

## Slide 22: OSI Model Layer 6 - Presentation (2)
Apple Filing Protocol
NetWare Core Protocol (Novell’s NCP)
NetBIOS (Based on any underlying protocol) NOTE: NetBIOS at this level is subject to some debate)

## Slide 23: OSI Model Layer 7 - Application (1)
Application Protocols use lower layers (usually 4 or 5)
Structure is specific to needs of individual application
Layer 4 (transport) for quick simple data
Layer 5 (Session) for validation or verification of delivery

## Slide 24: OSI Model Layer 7 - Application (2)
SMB (Microsoft’s Server Message Block)
NCP (Novell’s Netware Core Protocol)
Telnet - Remote access to hosts (TCP)
FTP - File Transfer Protocol (TCP)
HTTP/HTTPS-(Secure) HyperText Transport Protocol (TCP)
SMTP - Simple Message Transport Protocol (TCP)
SNMP - Simple Network Management Protocol (UDP)
DNS - Domain Name Service (UDP for Name Lookup, TCP for Zone Transfer)

## Slide 25: OSI Model Relationships - Abstract

## Slide 26: OSI Model Relationships Microsoft Networking

## Slide 27: OSI Model Relationships Internet Email

## Slide 28: OSI Model Relationships FTP (File Transfer) Session

## Slide 29: Encapsulation (How it fits together)
Each layer depends on the one(s) below it
Each layer treats the one(s) above as data
Each layer has its own error checking
Each layer “thinks” it’s communicating with its peer at the other side.
Each layer actually communicates with the ones immediately above and below it.

## Slide 30: Physical Layer - Details - LAN
802.5 - 4/16 Mb Token Ring - IBM Connectors
802.5 - 4/6 Mb Token Ring - MAU
FDDI - Fiber Distributed Data Interface
10Base5 - Thick Ethernet 10 Mb/s
10Base2 - Thin Ethernet 10 Mb/s
10BaseT - Twisted Pair 10 Mb/s Cat 3/4/5
10BaseFL - Multimode Fiber 10 Mb/s
100BaseT - Twisted Pair 100 Mb/s Cat 5/6
100BaseFL - Multimode Fiber 100 Mb/s
1000BaseT - Twisted Pair 1000 Mb/s Cat 5

## Slide 31: Physical Layer - Details - MAN
(Metropolitan Area Network)
Microwave Links (10/100 Mb/s)
802.11 - Wireless LAN, Frequency Hopping
Laser Links (10/100 Mb/s)
56K switched service (Interoperable w/ISDN based on entry in a central database)
ISDN (Integrated Services Digital Network)
56/64K dedicated service (Framing Dependent)
HSSI (High Speed Serial Interface)
Analog Modems (V.whatever - details later)

## Slide 32: Physical Layer - Details - WAN
(Wide Area Networking)
ISDN (Integrated Services Digital Network)
56/64K dedicated service (Framing Dependent)
Fractional/Full T-1 (64K/Channel 1.5 MB Full)
Fractional/Full T-3 (45 MB (15 T-1’s)
ISDN (Integrated Services Digital Network)
SMDS (Switched Multimegabit Data Services)
Satellite Links (High Latency)

## Slide 33: Datalink Layer - Details
ODI - NetWare Standard
NDIS 3 (Microsoft Standard)
Sockets (Berkeley Unix interface)
TLI (Transport Layer Interface) Unix SVR4
Shims (Sit on one datalink layer to make it look like another)

## Slide 34: IPX/XNS Packet Details
Immediate (for local network) Destination/Source MAC addresses
Optional framing (802.2, Ethernet II)
Packet Type
Destination network number, MAC address, and socket number
Originating network number, Mac address, and socket number
Application specific data

## Slide 35: Common numbering systems(1)
Decimal (Base 10)
Hexadecimal (Base 16)
Binary (Base 2)
Octal (Base 8) (Some older systems)

## Slide 36: Comparing Numbering systems (2)
Base 10 (decimal) uses digits 0-9 and has ones, tens, hundreds, thousands places etc.
Base 16 (hexadecimal) uses digits 0-9 and A-F and has ones, sixteen’s, two-hundred-fifty-six, and four-thousand-ninety-six places, etc.
Base 2 (binary) uses digits 0-1 and has one’s, two’s, four’s, eight's, sixteen’s, thirty-two’s, sixty-four’s, one-hundred-twenty-eight’s, etc.
Base 8 (octal) uses digits 0-7 and has one’s, eight’s, sixty-four’s, and five-hundred-twelve’s, places etc.

## Slide 37: Comparing Numbering systems (3)
Dec Hex Binary Dec Hex Binary
0 0 00000000 17 11 00010001
1 1 00000001 18 12 00010010
2 2 00000010 19 13 00010011
3 3 00000011 20 14 00010100
4 4 00000100 21 15 00010101
5 5 00000101 22 16 00010110
6 6 00000110 23 17 00010111
7 7 00000111 24 18 00011000
8 8 00001000 …. …. ….
9 9 00001001 126 7E 01111110
10 A 00001010 127 7F 01111111
11 B 00001011 128 80 10000000
12 C 00001100 129 81 10000001
13 D 00001101 …. …. ….
14 E 00001110 224 E0 11100000
15 F 00001111 252 FC 11111100
16 10 00010000 255 FF 11111111